## Slide 1: The door that opens by itself
Lesson 5 · A motor that listens to your sensor
JA05 STEAM and Service Learning · 23 Oct 2026
Notes: 100 minutes today. The new part is the servo: the first output that MOVES something. Open by telling the class the finished thing: a door that opens when somebody comes near, and that you can also open from your phone. Show your own working one if you have it built.

## Slide 2: Who cannot open a door?
Hands full
Shopping in both hands. No hand left for the handle.
Wheelchair
Pull the door, roll backwards, go through. Twice as hard.
Crutches
One hand holds you up. One hand is not enough.
Hospital
Touching handles moves germs from hand to hand.
An automatic door is not a luxury. For some people it is the difference between going in and going home.
Today you build one. Sensor sees a person · servo opens the door.
Notes: Spend three minutes here, not thirty seconds. Ask the class to name a door in school that is heavy. Ask who has pushed a trolley or carried a box through it. This is the service-learning hook: the same circuit they build today is the one a real accessible door uses. Do not decide the class project yet; we come back to it at the end.

## Slide 3: Today: 100 minutes
Files
0
Look back
8
Step 0
how a program runs
20
Step 1
34
Step 2
45
Step 3
you write angle_for()
56
Talk
84
100
min
Steps 0 to 2 are read-and-run. Step 3 is the one you write. Step 4 (phone) only if you get there.
Every group leaves with a servo that moves. That already counts as finished.
CHECKPOINT By minute 45 every group has a servo that moves to three positions.
Notes: Hold the clock. If Step 1 has not happened by minute 35, stop the whole class and wire the servo together. Step 4 is expendable; the closing discussion is not.

## Slide 4: Get today's files
Terminal
MacBook:~ s20xxxxxx$ cd ~/JA05
MacBook:JA05 s20xxxxxx$ ./get_latest.sh
Checking GitHub for new files...
Done. You have the latest files.
New folder: 20261023_L5
1
Saves anything you changed into my_work
2
Gets the newest files from GitHub
3
Never touches your ESP32
CHECKPOINT A folder 20261023_L5 appears in JA05.
STUCK? permission denied? Type: bash get_latest.sh
Your own code from last lesson is on the ESP32, not in JA05. It is safe.
Notes: Same one command as Lesson 4. Anyone whose JA05 folder is broken: rename it to JA05_old and clone again (Lesson 4 slide 4). Do not spend more than five minutes on git problems; pair that student with a neighbour and move on.

## Slide 5: How to use the code today
1
Bottom-right of Thonny says MicroPython (ESP32)
2
View > Files, then open JA05 > 20261023_L5
3
Right-click the step file > Upload to /
4
Double-click it under MicroPython device
5
Run (F5) without changes first
6
Change only Try it / YOUR CODE lines. Cmd+S saves on the ESP32
Don't type code from the slides
Slides show only PART of a program. The whole program is already in the file.
step1_servo_sweep.py · lines 20–21
This header tells you which file and which lines to look at.
Notes: Same rule as Lesson 4 and it worked: far fewer broken programs. If Thonny does not connect: Run > Configure interpreter > MicroPython (ESP32), choose the usbserial port. Click Stop to interrupt a running program.

## Slide 6: Look back: what did you build?
The sensor
sends out a sound,
times the echo
A number
e.g. 12.4 cm
YOUR function
leds_for()
gap_for()
The output
3 LEDs on,
fast beeps
The sensor and the LEDs are the easy half. The thinking happened in the middle box, and you wrote that part.
Tell your partner, 30 seconds each
What did your parking sensor do when a hand came close?
Then: what took you longest?
Wiring? The maths? Finding the file? Say which.
Notes: Do this before any new code. Take three or four answers out loud. Expect wiring to win; say that is normal and that today's wiring is only three wires. The point of the chain picture is that the sensor and the LEDs are bought parts, and the only thing that was theirs was the function in the middle. That is the thing we are about to do a third time.

## Slide 7: You have used functions all along
print("Hello") | Someone else wrote it | Shows text in the Shell
time.sleep(1) | Someone else wrote it | Waits one second
led.value(1) | Someone else wrote it | Turns the pin on
leds_for(12) | YOU wrote it | Gives back 3
again and
again, about
10 times a
second
The only new thing in Lesson 3 was this: you made one of your own.
Notes: Aimed at the students who think they have never seen a function. They have used three or four every lesson. Ask: who wrote print? Nobody in this room. Somebody wrote it once and everyone uses it. That is the whole idea.

## Slide 8: The parts of a function
def leds_for(distance):
def = I am making one
the name you choose
what goes IN
return 5 - int(distance // 5)
what comes OUT
Writing def does not run it. It only tells Python the recipe exists.
leds_for(12) runs it. distance becomes 12 inside, just for that one run.
Notes: The two boxes at the bottom are the misconception that costs most time: students write a function, press Run, see nothing happen, and think it is broken. Defining and calling are different moments. Also say: distance is a nickname that only exists inside the function, which is why leds_for(12) and leds_for(40) do not fight each other.

## Slide 9: Step 0: watch a function run
0
No wiring. Upload step0_functions.py, run it, and read the Shell from top to bottom.
step0_functions.py · lines 11–21
11 print("1. The program starts here")
12
13
14 def greet(name):
15 print(" Hello,", name)
16
17
18 print("2. greet is DEFINED. No hello yet.")
19
20 greet("Class 2A")
21 greet("Ms Chan")
CHECKPOINT Line 2 of the Shell appears BEFORE any hello.
STUCK? Nothing in the Shell? Press Run, not just save.
Terminal
1. The program starts here
2. greet is DEFINED. No hello yet.
Hello, Class 2A
Hello, Ms Chan
3. Two hellos: greet was CALLED
twice.
4. distance -> how many LEDs
12 cm -> 3 LEDs
Try it: delete the two greet(...) lines. The hellos stop, the rest still runs.
Notes: Twelve minutes. This file needs no hardware, so Track A groups and groups with a broken board can do it too. The Shell order is the lesson: message 2 prints before any hello, which proves that def does not run anything. Walk round and ask two or three students to read their Shell out loud.

## Slide 10: The order Python really does it
0
step0_functions.py · lines 11–23
11 print("1. The program starts here")
12
13
14 def greet(name):
15 print(" Hello,", name)
16
17
18 print("2. greet is DEFINED. No hello yet.")
19
20 greet("Class 2A")
21 greet("Ms Chan")
22
23 print("3. Two hellos: greet was CALLED twice.")
1
line 11
prints “1. The program starts here”
2
lines 14-15
SKIPPED. Python only remembers that greet exists
3
line 18
prints “2. greet is DEFINED …”
4
line 20
calls greet, jumps UP to line 15, prints, comes back
5
line 21
calls greet again. Line 15 runs a second time
6
line 23
prints “3. Two hellos …”
Line 15 never runs until something calls greet.
Python reads top to bottom, except when a call sends it somewhere else.
Notes: This is the slide to go slowly on. Put your finger on the Shell output from Step 0 and match it line by line against the numbers here. Step 2 is the one that surprises them: Python walks past the def without running the body. Ask: how many times does line 15 run? Twice, once per call, and the name is different each time.

## Slide 11: What happens when the ESP32 starts
Power on
boot.py
main.py
your program
or, while you are working:
you press Run (F5)
inside your program
read the sensor
decide (your function)
move the servo
again and again,
about 10 times
a second
while True:
Stop, or Ctrl+C breaks the loop. The finally: lines then tidy up.
The file lives on the chip. Unplug the Mac, use a power bank: it still runs.
main.py is the only name the ESP32 starts by itself. Any other name needs the Run button.
Notes: The bird's-eye slide. Three things they must leave with: (1) something has to start the program, either power-on through main.py or the Run button; (2) the work happens inside one loop that repeats about ten times a second, and their function is one box inside it; (3) the program is stored on the ESP32 itself, which is why it keeps running on a power bank. Lesson 4's main.py trick is the same idea: main.py contains one import line.

## Slide 12: Trace it: what does leds_for(12) give?
0
step0_functions.py · lines 27–35
27 def leds_for(distance):
28 return max(0, min(5, 5 - int(distance // 5)))
⋮
35 answer = leds_for(12)
1
distance becomes 12
the number on line 35
2
12 // 5 is 2
how many whole 5 cm fit into 12
3
5 - 2 is 3
max/min keep it 0 to 5
4
gives back 3
line 35 puts 3 into answer
Now you. On paper, no computer.
leds_for(40) gives back?
leds_for(2) gives back?
How many times does line 28 run when the for loop on line 32 goes round five times?
Which line of your Lesson 3 program decided WHEN the LEDs change? Was it inside leds_for?
gap_for(20) gave 0.4 s. What gives gap_for(10)?
Notes: Answers: leds_for(40) is 0, because 5 - 8 is negative and max(0, ...) pulls it up to 0. leds_for(2) is 5. Line 28 runs five times, once per call: a function body runs once per call, not once in the program. The Lesson 3 question is the important one: the deciding line was in the main loop, not inside leds_for, because the function only answers a question. gap_for(10) is 0.2 s. Two minutes on paper, then take answers.

## Slide 13: Self-check: tick what you can do
I can read a line like leds_for(12) and say what it gives back
Step 0, slide before this
I can say the difference between writing def and calling the function
Step 0: the Shell order
I can change a number inside a function and predict what happens
Step 0 Try it lines
I can write the inside of a function when I am told what goes in and out
that is today's Step 3
Cannot tick one? Say so now. Three people here can explain it, and one of them is sitting next to you.
Notes: Ask for a show of hands on each line, lowest first. Do not move on if more than about a third cannot tick line 2: go back to the Shell output in Step 0 and read it together. Line 4 is deliberately not ticked yet for most of the class; it is what Step 3 is for, and saying so lowers the stakes.

## Slide 14: You have written this twice already
Lesson 3
leds_for(distance)
how many LEDs?
gives back: 0 to 5
Lesson 4
gap_for(distance)
how long to wait?
gives back: 0.1 to 0.5 s
Today
angle_for(distance)
which angle?
gives back: 0 or 90
The same shape every time
distance -> your function -> one decision
A number goes in. You decide what comes out. The rest of the program is already written.
Notes: Make the pattern explicit: this is the third time, so students should recognise the job before they see the file. Ask one student to say in words what leds_for did. The new part today is only that the answer drives a motor instead of an LED.

## Slide 15: Pick your track
Does your LED bar light up when your hand gets closer?
A
Not yet
Wire the sensor: Lesson 3 PDF page 25
Run 20261009_L3/step5_solution.py
Then start Step 1 with everybody else
B
Yes, it works
Start at Step 1: wire the servo
Step 2: set_angle()
Step 3: you write angle_for()
You do not need the buzzer today. The servo is the new part for everyone.
Notes: Track A is shorter today than last lesson: they only need the sensor, not the buzzer, to join. Aim to have everyone on Step 1 by minute 25. Seat a finished group next to each Track A group.

## Slide 16: Track A: catch up fast
A
1
Upload the Lesson 3 files you need to the ESP32
2
Check the LEDs: step3a_check_leds.py
3
Add the sensor: Lesson 3 PDF, page 25
4
Run step4_ultrasonic_print.py, then step5_solution.py
5
LED bar works? Go straight to Step 1
CHECKPOINT Hand closer, more LEDs on.
Notes: Use the published solution so these groups are not still debugging at minute 60. Lesson 3 PDF page 25 is the sensor wiring, page 30 the troubleshooting table.

## Slide 17: A servo is an output that moves
Part | You say | It does
LED | value(1) | light, on or off
Buzzer | value(1) | sound, on or off
Servo | an angle: 0 to 180 | turns there and HOLDS it
It holds the angle. Let go of the door and it stays open.
Inside: a small motor, gears, and a sensor that checks where the arm is, thousands of times a second.
0°
90°
Same servo. Two angles.
Notes: Pass a servo round if you have a spare. Turn the horn gently by hand with the power off so students feel the gears. Key idea for today: an LED has two states, a servo has 181. That is why we need a function that chooses one.

## Slide 18: Wire the servo - read this first
Servo wire | Goes to
brown or black | GND
red | 5V (never 3V3)
orange or yellow | GPIO26 (IO26)
IO26 is on the left side, one below IO25.
The sensor also needs 5V. Use the red rail on the breadboard so one pin feeds both.
ESP32
5V
GPIO26
GND
servo
red
orange
brown
Red goes to 5V. On 3V3 the ESP32 resets when the servo moves.
Notes: Stop the class and show this on a real board before anyone runs code. The 3V3 mistake is the one that eats twenty minutes: the board resets, Thonny disconnects, and students think their code is wrong. Also tell them to tape the servo down or hold it; a loose servo walks off the desk. If a group's board still resets on 5V over USB, give them a power bank or a powered hub.

## Slide 19: Step 1: make it move
1
Upload step1_servo_sweep.py and run it without changing anything.
step1_servo_sweep.py · lines 20–34
20 servo = PWM(Pin(26))
21 servo.freq(50)
⋮
29 servo.duty_u16(1638)
30 print("0 degrees")
31 time.sleep(1)
32
33 servo.duty_u16(4915)
34 print("90 degrees")
CHECKPOINT The horn jumps to three positions, then back.
STUCK? Nothing moves? Check orange on IO26, red on 5V.
ESP32
5V
GPIO26
GND
servo
red
orange
brown
Red goes to 5V. On 3V3 the ESP32 resets when the servo moves.
Notes: The horn must be loose or off for Step 1: if it is screwed on and jammed against the servo body the gears grind. Expect a buzz at 180 degrees on some servos, which is why the file stops at 8100 and not 8192. Ask what duty_u16 numbers mean before explaining: nobody can guess, which is exactly the point of Step 2.

## Slide 20: Read the code: Step 1
1
step1_servo_sweep.py · lines 17–26
17 from machine import Pin, PWM
18 import time
19
20 servo = PWM(Pin(26))
21 servo.freq(50)
22
23 # angle duty_u16
24 # 0 1638
25 # 90 4915
26 # 180 8100
Line 20
PWM switches GPIO26 on and off. Same tool as the LED brightness and the buzzer pitch.
Line 21
50 times a second. A servo only listens at this speed.
Line 23–26
The duty number that means each angle. Nobody remembers these.
Line 29
duty_u16(1638): go to 0 degrees and hold.
Predict, then try
Which number would send it to 45 degrees? Try your guess on line 29.
Notes: Answer: about 3276, halfway between 1638 and 4915. Most groups will guess by halving, which is the right instinct and leads straight into set_angle(). PWM has now meant three things: brightness in project 4, pitch in Lesson 4, position today. Same tool, different meaning.

## Slide 21: Step 2: say the angle, not the number
2
No rewiring. Upload step2_servo_angle.py and run it.
step2_servo_angle.py · lines 21–27
21 def set_angle(deg):
22 if deg < 0:
23 deg = 0
24 if deg > 180:
25 deg = 180
26 duty = MIN_DUTY + deg * STEP_PER_DEGREE
27 servo.duty_u16(int(duty))
step2_servo_angle.py · lines 32–34
32 print("angle:", angle)
33 set_angle(angle)
34 time.sleep(0.8)
CHECKPOINT It stops at every angle in your list.
Why bother?
Before
servo.duty_u16(4915)
After
set_angle(90)
Both do the same thing. Only one of them can be read by a human six weeks later.
STUCK? Buzzing and stuck? Free the horn.
Notes: This is a software idea, not a hardware one: give the ugly number a name and hide it in a function. The for loop over a list is also new-ish; point out that the servo visits each item in order. Try it: students put their own angles in the list on line 32.

## Slide 22: Read the code: set_angle()
2
step2_servo_angle.py · lines 17–27
17 MIN_DUTY = 1638
18 STEP_PER_DEGREE = 36.4
19
20
21 def set_angle(deg):
22 if deg < 0:
23 deg = 0
24 if deg > 180:
25 deg = 180
26 duty = MIN_DUTY + deg * STEP_PER_DEGREE
27 servo.duty_u16(int(duty))
Line 17
1638 is 0 degrees: the smallest signal the servo accepts.
Line 18
Every degree adds 36.4. So 90 degrees adds about 3276.
Line 22–25
Guard rails: nothing below 0, nothing above 180.
Line 26–27
int() because duty_u16 only takes whole numbers.
Work it out
1638 + 90 × 36.4 = ? Compare it with the table in Step 1.
What does set_angle(500) do? Why does nothing break?
Notes: Answers: 1638 + 3276 = 4914, which is the 4915 from the Step 1 table, one off from rounding. set_angle(500) is cut down to 180 by lines 24-25, so the servo goes to its end stop instead of being asked for something impossible. Ask why guard rails matter when a sensor is the thing calling the function: a bad reading must not break the machine.

## Slide 23: How should the door behave?
SHUT · 0°
Nobody there
OPEN · 90°
Somebody within 15 cm
OPEN · 90°
They passed: open 2 s more
approach
open
walk through
wait 2 s
shut
Think: why must the door wait before it shuts? What happens to a slow walker if it shuts the instant the sensor stops seeing them?
Notes: Take answers before showing the code. The waiting time is called hold-open time and real accessible doors are required to have one; a door that shuts the moment you pass the sensor hits people with walking frames. In our file it is HOLD_LOOPS = 20, about 2 seconds. It also quietly fixes a jitter problem: without it the servo flickers open and shut at exactly 15 cm.

## Slide 24: Step 3: you write angle_for()
3
step3_auto_gate.py · lines 32–35
32 OPEN_ANGLE = 90
33 CLOSED_ANGLE = 0
34 NEAR_CM = 15
35 HOLD_LOOPS = 20
step3_auto_gate.py · lines 71–82
71 def angle_for(distance):
⋮
76 # ----- YOUR CODE STARTS HERE -----
⋮
80 # Use OPEN_ANGLE and CLOSED_ANGLE, not 90 and 0.
81
82 return CLOSED_ANGLE # replace this line
Replace line 82 only. Do not change any other line.
distance | angle_for() gives back
None (sensor saw nothing) | CLOSED_ANGLE
less than NEAR_CM | OPEN_ANGLE
anything else | CLOSED_ANGLE
Watch out: the sensor gives None sometimes. Test for it FIRST or the program crashes.
CHECKPOINT Hand near: opens. Hand away: shuts 2 s later.
STUCK? Never opens? Line 82 is still CLOSED_ANGLE.
Notes: Thirty minutes on this. Do not give the answer: give the table. Common wrong answers, all worth letting them hit: (1) forgetting None, which crashes with TypeError the first time the sensor misses; (2) writing 90 and 0 instead of OPEN_ANGLE and CLOSED_ANGLE, which works but breaks when you change the constant; (3) testing distance > NEAR_CM and swapping the two answers, which is also correct. Full version in teacher_solutions/20261023_L5.

## Slide 25: Read the code: what the loop does
3
Measure distance
line 90
Show LED bar
line 91
angle_for(distance)
line 93 - YOURS
open? reset hold = 20
line 94
hold bigger than 0?
line 96
Door OPEN, hold = hold - 1
lines 97-98
Door SHUT
line 100
yes
no
hold counts down 20 times, and the loop waits 0.1 s each time.
20 × 0.1 s = 2 seconds of staying open.
Your function is used in one place only: line 93.
Notes: Walk the loop out loud with a volunteer's hand in front of the sensor. Key question: what happens the moment the hand goes away? angle_for returns CLOSED_ANGLE, so hold stops being reset, counts down from 20, and only then the door shuts. Students who delete the hold see the twitch straight away: that is a good thing to let happen once.

## Slide 26: The whole circuit
ESP32
5V
GPIO13
GPIO14
GND
GPIO26
GPIO16
GPIO17
GPIO18
GPIO19
GPIO23
GND
VCC
Trig
Echo
GND
HC-SR04
servo
Dashed red: the servo's power wire goes to the breadboard's 5V rail, the same rail as the sensor.
Outlined: every pin used today. Purple = servo.
Notes: Reference slide: leave it up while groups work. The servo's red wire shares the 5V rail with the sensor, shown dashed. Everything from Lessons 3 and 4 stays exactly where it was.

## Slide 27: Step 4: open it from your phone
4
Your phone
class Wi-Fi
your ESP32
the servo
Every board gets its own address, like 10.0.0.37. Yours is printed in the Shell when the program starts.
Terminal
Connecting to css_STEAM ...
Connected. Open this on your phone: http://10.0.0.37/
Your phone must be on the class Wi-Fi. On mobile data the page will never load: the two are not on the same network.
The door is SHUT
Sensor sees: 42 cm
OPEN
CLOSE
10.0.0.37
Notes: This is the IoT idea in one slide: the board is a tiny web server on the school network, and the phone is just a browser. Nothing goes to the internet; the page never leaves the school. If the network blocks device-to-device traffic the page will not load, in which case skip Step 4 and go to the discussion.

## Slide 28: Step 4: type the Wi-Fi name yourself
4
step4_web_gate.py · lines 16–17
16 SSID = ""
17 PASSWORD = ""
SSID = "css_STEAM" PASSWORD = "steam2026!"
step4_web_gate.py · lines 110–115
110 while True:
111 client, address = server.accept()
112 request = client.recv(1024).decode()
113
114 if "GET /open" in request:
115 is_open = True
1
Open your copy under MicroPython device
2
Type both lines exactly, keep the quotes
3
Cmd+S saves it on the ESP32, not in JA05
4
Run it. Read the IP in the Shell
5
Open that address on your phone. Press OPEN
CHECKPOINT The horn moves when you tap OPEN.
STUCK? Wi-Fi FAILED? Check both quotes are still there.
Notes: The Wi-Fi name and password are on Lesson 1 slide 14 (SSID css_STEAM). Put that slide up, or read it out. The file ships with the two lines empty, so each student types them into their own copy on the ESP32. Remind them it is the copy under MicroPython device, the one whose tab name is in square brackets, not the file in JA05. Line 111 is where the program waits for the phone: nothing else happens until a page is requested, which is why the distance only updates when the page refreshes. Fast groups get the Try it on line 126: open the door when the page asks OR when the sensor sees somebody. Answer is in teacher_solutions.

## Slide 29: Who is your door for?
Sensor only
Opens for anybody who comes near. Nobody has to touch anything.
Phone only
Somebody decides who comes in. Good for a gate, bad for a shop.
Both
Opens by itself, and a person can override it.
Talk to the person next to you: name one door in this school.
Who struggles with it, and when?
Would your sensor see them in time?
What would go wrong at the busiest minute of the day?
Notes: Two minutes in pairs, then take three answers. Write the doors on the board: this list is the start of choosing the class service-learning project. Push on the third question: a door that opens for everyone walking past in a corridor is useless, which is a design problem, not a coding one.

## Slide 30: What did you reach today?
A
LED bar works
0
Functions
1
Servo moves
2
set_angle()
3
Door opens
4
On your phone
A servo is an output that holds a position. PWM meant brightness, then pitch, now angle.
Third time: a function turns a distance into a decision. def makes it, the brackets run it.
A door that shuts too fast is a door that hurts somebody. Hold-open time is part of the design.
Next: pick the real problem we build for.
Notes: Show of hands for each step. Unplug USB before pulling any wires. Ask them to leave the servo wired if the kit stays in the room.