## Slide 1: How loud is this room?
Lesson 6 - A meter that remembers
JA05 STEAM and Service Learning - 30 Oct 2026
Notes: 100 minutes. Today the device gets a memory. Open by asking the class how loud this room is right now, and let them argue. Nobody can answer it with a number. That is the whole lesson: turn an argument into a measurement, then count how often it happens.

## Slide 2: Who does noise hurt?
Hard of hearing
A hearing aid makes everything louder, the noise included.
Trouble focusing
Some people cannot filter a room out. The noise is all of it.
The teacher
Talking over a loud room all day. Voices give out.
Everybody
You stop hearing it. You do not stop being tired by it.
Nobody wins an argument about noise. Somebody says it is fine, somebody says it is not.
A number ends the argument. Today you build the thing that makes the number.
Notes: Three minutes. Ask for a show of hands: who finds this room too loud to think in? The split in the room is the point. Service-learning hook: the meter is evidence, and evidence is what you need before you ask anyone to change anything. Do not pick the class project yet, that is 4 November.

## Slide 3: Today: 100 minutes
Files
Steps 0
listen, then test the parts
Step 1
you write level_for()
State
a program that remembers
Step 3
you write the counter
Real run
0
8
28
40
58
82
100
min
Three new ideas today: measuring something that will not hold still, a program that remembers, and how to find a bug on purpose instead of by luck.
CHECKPOINT By minute 40 every group has an LED bar that follows their voice.
Notes: The purple block in the middle is teacher-led. Everything before it is hands on, everything after it needs it. If you are running late at minute 58, cut Step 4 and the LCD, never the state block: Step 3 is unwriteable without it.

## Slide 4: Get today's files
Terminal
MacBook:~ s20xxxxxx$ cd ~/JA05
MacBook:JA05 s20xxxxxx$ ./get_latest.sh
Checking GitHub for new files...
Done. You have the latest files.
New folder: 20261030_L6
1
Saves anything you changed into my_work
2
Gets the newest files from GitHub
3
Never touches your ESP32
CHECKPOINT A folder 20261030_L6 appears in JA05.
STUCK? permission denied? Type: bash get_latest.sh
Step 4 also needs lcd128_32.py and lcd128_32_fonts.py uploaded. They are in the folder.
Notes: Same command as every lesson. Five minutes maximum on git trouble, then pair the student with a neighbour and move on.

## Slide 5: The seven files, in order
step0_read_sound.py
RUN
The number jumps when you clap
step0b_test_parts.py
RUN
All three tests pass
step1_peak_level.py
WRITE 1 line
The LED bar follows your voice
step2_counter_demo.py
RUN
One count sticks at 1, the other counts up
step2b_find_the_bug.py
MOVE 1 line
It prints 3
step3_noise_counter.py
WRITE 2 lines
One clap adds exactly 1
step4_lcd_report.py
RUN, if you get there
The screen matches the LEDs
you do
you should see
Every file says WHAT YOU DO at the top. RUN means run it unchanged: reading it IS the work.
Notes: Put this up for one minute and leave the slide number on the board. The two complaints this prevents: which file now, and am I supposed to be typing. Say out loud that four of the seven files are run-and-read, and only three ask for typing. Students who think every file needs editing will break the demos.

## Slide 6: Every file has the same five parts
1
SETUP
the pins and the sensor
lines 20-30
2
NUMBERS YOU CAN CHANGE
QUIET, LOUD, COOLDOWN
lines 33-40
3
FUNCTIONS
the thinking: loudness(), level_for()
lines 43-68
4
THE MEMORY
made once, before the loop
lines 70-75
5
THE LOOP
again and again, until you stop it
lines 77-100
line numbers from step3_noise_counter.py
You only ever touch two parts
A function in part 3, or the loop in part 5. Parts 1 and 4 you read, never edit.
Look for these
>>>>> YOUR CODE
STARTS HERE >>>>>
<<<<< YOUR CODE
ENDS HERE <<<<<
Scroll until you see the arrows. Your work goes between them, and nowhere else.
Notes: Two minutes, and it pays for itself in Step 3. Open step3_noise_counter.py on the projector and scroll it slowly while they match the five banners. The point to say out loud: every file today has this shape, so once you can find part 5 you can find it in all of them. The arrow markers mean nobody has to hunt for a comment that says YOUR CODE.

## Slide 7: Wire it: microphone + Lesson 3 LEDs
ESP32
3V3
SENSOR VP
GPIO16
GPIO17
GPIO18
GPIO19
GPIO23
GND
V
G
S
sound sensor
S = analog out
The blue screw
sets how big the signal reaching S is. It does NOT set what counts as loud: your code does that. Set it once, leave it.
Only these pins today. Leave the ultrasonic sensor, the buzzer and the servo in the box.
S, V, G in that order on the module.
SENSOR VP is the pin under EN.
Notes: Most groups still have the Lesson 3 LED bar built, so this is three new wires. Walk the room and check AO against DO before anybody runs anything: a module wired on DO gives 0 and 4095 and nothing in between, and the group will chase that bug for twenty minutes.

## Slide 8: Step 0: run it and listen
0
step0_read_sound.py · lines 29–37
29 mic.width(ADC.WIDTH_12BIT) # answer as 0 to 4095
30
31 try:
⋮
34 print(value)
35 time.sleep(0.2)
36
37 finally:
CHECKPOINT The number jumps when you clap.
STUCK? Always 0? S is on SENSOR VP, the pin under EN.
ATTN_11DB means measure the whole 0 to 3.3 V. WIDTH_12BIT means answer as 0 to 4095.
Terminal
quiet room
6 11 4 9 7 5
8 6 12 5 9 6
one clap
7 1240 843 96
310 44 9 7
Your numbers will not match these. They depend on the gain screw. That is the point of Step 0b.
Notes: Ten minutes. Everyone must see the number refusing to sit still in a silent room. Do not explain why yet, the next slide does that. Collect two or three numbers from different groups and write them on the board: they will not match, which is useful.

## Slide 9: One reading lies
the gap
quiet
talking
what
A microphone reports where its diaphragm is, right now
loud
means it swings further, not that the number gets bigger
so
take 50 readings fast. Loudest minus quietest is the loudness
A single reading is a photograph of a moving thing. You need the whole swing.
Notes: Five minutes, teacher led. Shake your hand fast in front of the class and ask how far it moved: one glance cannot answer, you need to watch for a moment and take the widest point. Same for the microphone. That is why the code takes 50 readings and subtracts.

## Slide 10: Step 0b: run the three part tests
0b
Terminal
TEST 1 of 3: the LEDs, one at a time.
LED on GPIO 16
LED on GPIO 17
...
TEST 2 of 3: the sensor, in silence.
lowest: 4 highest: 37 gap: 33
TEST 3 of 3: the sensor, with noise.
lowest: 5 highest: 1690 gap: 1685
1
All 5 LEDs lit? If not, that LED or its resistor
2
Quiet gap under about 60? If not, turn the screw back
3
Clap gap in the hundreds? If not, check S, then the screw
CHECKPOINT All three tests pass.
Pass all three, and any bug after this is in your code, not your wiring.
Notes: Ten minutes, and it is worth every one. This file is the worked example of the idea on the next slide: three parts, three separate tests, each answered by looking. After today, the sentence it does not work should get the reply which test failed.

## Slide 11: Test the parts, not the whole
INPUT
the sensor
test it alone:
Step 0b, tests 2 and 3
DECIDE
your function
test it alone:
print(level_for(500))
OUTPUT
the LEDs
test it alone:
Step 0b, test 1
You can test the middle box with no sensor and no noise at all, because it is a function. That is what functions are for.
Three parts, three tests. A broken whole becomes one broken part, and a broken part is a wire you can look at.
Notes: Keep this short, three minutes, because Step 0b already showed it. The line that matters is the middle one: print(level_for(500)) runs in the Shell with no hardware. Several students will not believe you can test a function without the sensor until you do it in front of them.

## Slide 12: Step 1: you write level_for()
1
step1_peak_level.py · lines 53–60
53 def level_for(gap):
54 """Turn a loudness gap into how many LEDs: 0 to 5."""
55 # >>>>> YOUR CODE STARTS HERE >>>>>
56 # One line. Under QUIET -> 0 LEDs. Over LOUD -> 5 LEDs.
57 # In between, spread it out. Same shape as leds_for()
58 # in Lesson 3 and angle_for() in Lesson 5.
59 return 0
60 # <<<<< YOUR CODE ENDS HERE <<<<<
loudness() is given. It hands level_for() one number.
step1_peak_level.py · lines 40–50
40 def loudness():
41 """SAMPLES readings fast. Loudest minus quietest."""
⋮
49 highest = value
50 return highest - lowest
quiet
gap under QUIET: 0 LEDs
loud
gap over LOUD: 5 LEDs
between
spread it across 1 to 4
CHECKPOINT The bar follows your voice.
STUCK? All 5 lit in silence? QUIET is too low for this room.
Notes: Twelve minutes. They have done this shape three times, so most groups get it in five. The honest difficulty is not the maths, it is that QUIET and LOUD were guessed in a different room: tell groups to use their own Step 0b numbers. A group whose bar sits at 5 has not got a bug, they have a room.

## Slide 13: A loop forgets
while True:
read the microphone
work out the level
light the LEDs
round and round, ten times a second
Every round starts the same way
The loop does not know this is round 400. It does not know the room was loud a second ago. It knows nothing except what you stored.
State
What the program knows right now, because of what happened before. A loop has no memory of its own. You give it one.
Notes: Start of your teaching block, minute 40. Say the definition and leave it on the board for the rest of the lesson. The reason this matters today and did not matter in Lesson 5: the door reacted to what the sensor says right now, and the meter has to react to what has happened since the program started. Counting is impossible without memory.

## Slide 14: Inside or outside the loop?
WRONG
while True:
count = 0
count = count + 1
print(count)
Terminal
1
1
1
1
1
RIGHT
count = 0
while True:
count = count + 1
print(count)
Terminal
1
2
3
4
5
One line moved. Everything changed.
Notes: The slide the whole lesson turns on. Ask before you explain: which one counts? Then ask why the left one is stuck at 1. The answer you want: count = 0 runs again every round, so the old value is thrown away. Use the word box if it helps: the left program makes a new box each round, the right one keeps adding to the same box.

## Slide 15: Step 2: run it and watch
2
step2_counter_demo.py · lines 17–28
17 print("WRONG: count is made again every time round the loop")
18 for round_number in range(1, 6):
19 count = 0 # made again, old value lost
20 count = count + 1
21 print(" round", round_number, "count is", count)
⋮
24 print("RIGHT: count is made ONCE, before the loop")
25 count = 0 # made once, the loop adds to it
26 for round_number in range(1, 6):
27 count = count + 1
28 print(" round", round_number, "count is", count)
CHECKPOINT The first count never passes 1. The second counts to 5.
No wiring. This one runs even if your circuit is in pieces.
Terminal
WRONG: count made every round
round 1 count is 1
round 2 count is 1
round 3 count is 1
RIGHT: count made once
round 1 count is 1
round 2 count is 2
round 3 count is 3
Notes: Eight minutes. Everyone runs it, nobody edits it yet. Then ask the Try it question at the bottom of the file: move shouts = 0 inside the loop and predict before running. Prediction first, every time.

## Slide 16: Remembering the LAST one
2
2
7
+1
8
2
9
+1
9
2
loud readings: 4
loud moments: 2
The memory, in four lines
is_loud = value > LOUD
if is_loud and not was_loud:
shouts = shouts + 1
was_loud = is_loud
not was_loud is the whole trick. Count only where quiet turns into loud, not every round it stays loud.
Notes: Ask the question before showing the answer: four readings are loud, so why is the count 2? Someone will say because two shouts. Push them to say which reading starts a shout: the one where the round before was quiet. Then the code line reads itself. The last line, was_loud = is_loud, is the one they forget in Step 3.

## Slide 17: Step 2b: move one wrong line
2b
step2b_find_the_bug.py · lines 14–26
14 readings = [1, 2, 8, 9, 1, 7, 1, 1, 6, 6, 2]
15 LOUD = 5
16
17 was_loud = False
18
19 for value in readings:
20 count = 0
21 is_loud = value > LOUD
22 if is_loud and not was_loud:
23 count = count + 1
24 was_loud = is_loud
25
26 print("Loud moments:", count)
It prints 0. The right answer is 3. One line is in the wrong place.
1
Run it. What does it print?
2
Add a print() inside the loop
3
Which line throws away what it knew?
4
Change ONE line. Run again
STUCK? Do not rewrite the file. Find the line.
Five minutes, in pairs.
Notes: Five minutes, strictly. Pairs, one screen. The bug is count = 0 sitting inside the for loop. Do not let a pair rewrite the program from scratch, that defeats the exercise: the skill is locating a line, not replacing code. Ask the first pair who finds it to say how they found it, not what the answer is.

## Slide 18: Self-check: state
I can say what a program forgets each time round a loop
slide: a loop forgets
I can say why count = 0 must sit outside the loop
Step 2, the two Shells
I can say why was_loud is needed to count moments
slide: remembering the last one
I can find a bug like that in someone else's code
Step 2b
Step 3 is unwriteable without these four. Say now if one is missing.
Notes: Hands up on each line, lowest first. If more than a third cannot tick line 2, go back to the two Shells and read them together. This is the gate: students who cannot tick 2 and 3 will not write Step 3, they will copy a neighbour and learn nothing.

## Slide 19: When it does not work
1
Does it run at all?
Red text names a line number. Open that line first.
2
Go back to the last version that worked
Step 2 ran, Step 3 does not? The bug is in what you changed.
3
Change one thing. Then run
Two changes at once and the result teaches you nothing.
4
Cut the program in half
Input, decision, or output? Test each one alone.
5
Make the invisible visible
print() the value you are guessing about.
Starting over is not number 6. It throws away the working half as well.
Notes: Five minutes, and keep it on screen for the rest of the lesson. Rung 2 is the answer to the question students always ask: if it broke after Step 3, do I start again? No. Copy the last file that worked and re-apply the change in smaller pieces. Rung 3 is the one they break most: they change three things, it works, and they cannot say why.

## Slide 20: Where exactly is it wrong?
The count races up while somebody talks | not was_loud is missing | you are counting readings, not moments
The count never moves at all | was_loud = is_loud is missing | the memory never updates
The count is stuck at 1 | loud_count = 0 is inside the loop | it is made again every round
The count climbs in a silent room | QUIET is too low for this room | not a bug. Measure your room
What you see
The usual cause
Why
Symptoms, not solutions. Match what you see, then go and look at that line yourself.
Notes: Put this up while they work on Step 3 and leave it there. It is deliberately phrased as symptom first, because that is how a student arrives: not knowing the cause. Do not read it out, let them find their row.

## Slide 21: Step 3: write the counter
3
step3_noise_counter.py · lines 84–97
84 is_loud = level >= TOO_LOUD_LEVEL
85 now = time.time()
86
87 # >>>>> YOUR CODE STARTS HERE >>>>>
88 # Line 1: count a new loud moment. Only if the room
89 # was quiet before, and only if COOLDOWN seconds
90 # passed since the last one. Add 1 to loud_count,
91 # then set last_count_time = now.
92 if False:
93 pass
94
95 # Line 2: remember is_loud for next time round.
96
97 # <<<<< YOUR CODE ENDS HERE <<<<<
Two lines. The hard part is already decided: count a moment only where quiet turns into loud.
now
time.time() gives seconds
COOLDOWN
2 seconds before a new moment can count
then
remember today's answer for next round
CHECKPOINT One clap adds exactly 1.
STUCK? Count racing? was_loud is missing.
Shout for five seconds. Still 1? Correct.
Notes: Twenty-four minutes, the main task. Walk the room with one question: show me where your program remembers. Groups who get it early go to Step 4 or run a real ten-minute measurement. Do not give out the two lines; give the Step 2 output back instead, they have already seen the answer there.

## Slide 22: What the meter remembers
3
step3_noise_counter.py · lines 70–75
70 # ===== 4. THE MEMORY: made once, before the loop =====
71 # The program's memory. Made ONCE, before the loop.
72 loud_count = 0
73 was_loud = False
74 last_count_time = 0
75
loud_count
how many loud moments so far
was_loud
was it loud LAST round?
last_count_time
when the last moment was counted
Three boxes, made once
Everything else in the program is worked out fresh each round. These three are the only things that survive from one round to the next.
Predict first: if you delete the COOLDOWN check, what does one clap do?
A clap is not one smooth sound. The level dips in the middle of it, so the room goes loud, quiet, loud, and the count goes up twice. COOLDOWN is what stops that.
Notes: Use this when groups start finishing. The predict question is worth asking even of a group whose code already works: most of them put COOLDOWN in because the file told them to, not because they know what it fixes.

## Slide 23: Step 4: run it with the LCD
4
step4_lcd_report.py · lines 62–70
62 def show(level):
63 for i in range(5):
64 leds[i].value(1 if i < level else 0)
65
66
67 def draw(level, count):
68 """Redraw the LCD. 4 rows, 18 characters each."""
69 lcd.Clear()
70 lcd.Cursor(0, 0)
1
Upload lcd128_32.py and the fonts file too
2
LCD: SDA to GPIO21, SCL to GPIO22
3
Run it. The screen shows level and count
CHECKPOINT The bar on screen matches the LEDs.
Noise level: 3
[###..]
Too loud: 7
The LCD from Lesson 1, doing a real job this time.
Only redraw when it changed. Clearing the screen ten times a second makes it flicker and slows the whole loop.
Notes: Stretch, not core. Groups that reach it have time to spare. The redraw-only-on-change idea is worth pointing out to them: it is the first time they have had to care that an output is slow.

## Slide 24: Say level, not decibels
Honest
"The room reached level 4 eleven times in this lesson."
Not honest
"The room was 85 decibels."
A phone app will disagree with you, and the phone will be right.
Nobody calibrated this sensor against a known sound. It measures a gap that follows loudness. That is enough to compare one lesson with another, and not enough to put a unit on.
Measuring something is easy. Saying exactly what you measured is the hard part, and it is the part people believe.
Notes: Four minutes, and do not skip it. A student will check the meter against a phone app this week and find it disagrees. Better they hear the reason from you first. This is also the science point of the lesson: an uncalibrated instrument can still compare, it just cannot name a unit.

## Slide 25: Ten real minutes
1
Run the meter for the last ten minutes of this lesson
2
Do not tell the class it is running
3
Write the count on the board at the end
4
Write it down. You will need it on 4 November
Talk to the person next to you
Who decides what too loud means? You set TOO_LOUD_LEVEL yourself.
A meter that beeps when the room is loud: quieter room, or louder?
Who in this school would actually use this? Name a person or a room.
What would make somebody trust your number?
The number on the board is evidence. On 4 November you pick the problem you will build for, and evidence beats opinions.
Notes: Run the meter yourself from minute 82 if the class is still working. The second discussion question is the real one: an alarm that shames a room usually makes it louder, and the class will get there on their own. Carry the answers to 4 November, and make somebody write the count down, because the next lesson after that is 27 November.

## Slide 26: What did you reach today?
0
Heard the room
0b
Tested the parts
1
level_for()
2
A program that remembers
3
Counted the moments
4
On the screen
One reading lies. Fifty readings, loudest minus quietest, tell the truth.
State is what the program knows because of what happened before. Made once, outside the loop.
A broken whole is three parts. Test each one alone and the bug has nowhere to hide.
Next, 4 November: pick the problem, and bring the number you measured today.
Notes: Two minutes. Ask one group to say their count out loud before they pack up. Remind them 4 November is a Wednesday, and that after it the next lesson is 27 November, so anything not written down is gone.